## Slide 1: Influence of synthetic vegetation on suspended sediment capture in laboratory flume experiments
Justin Nghiem
2018-19 Undergraduate Honors Thesis
Department of Geography, UC Berkeley
Advisor: Laurel Larsen

## Slide 2: Motivation
Coastal wetlands are facing historically rapid land loss
Mississippi Delta has lost over 5000 km2 of wetlands since 1930s
Relative sea level rise accelerates loss

## Slide 3: Motivation
Strategy: vegetation enhances retention of transported sediment load
  Based on previous studies [Palmer et al., 2004; Wu et al., 2011; Fauria et al., 2015]
Mathematical models to predict particle capture are valuable tools for wetland management
  Empirical models of Palmer et al. [2004] and Fauria et al. [2015]

## Slide 4: Research Questions
How well do existing models of suspended particle capture by vegetation stems perform?
  Are there important but unaccounted parameters?
For specific conditions, what is the influence of vegetation on suspended particle capture in wetlands?
How do we respond to these questions?

## Slide 5: One method: Flume experiments

## Slide 6: Background: General Terms
Particle capture – general removal of sediment particles from transport in the flow
Collectors – vegetation stems (or vegetation-like objects) in the flow; their surfaces “collect” particles from the flow
Suspended load – sediment transported in a flow in suspension

## Slide 7: Background: Particle capture mechanisms
Gravitational settling
Direction interception
Diffusional deposition – turbulence, Brownian motion
Inertial impaction – divergence from flowlines

## Slide 8: Background: Effective capture efficiency
Quantifies probability/overall rate of particle capture

## Slide 9: Background: Suspended load model
In practice, fit an exponential model, a solution of an advection-diffusion equation [Fauria et al., 2015]
where:

## Slide 10: Background: Particle capture rate, k
Particle capture rate quantifies how fast sediment concentration declines
May be decomposed as
Key: separate effects of settling and collectors
where:

## Slide 11: Background: Parameter Summary
1. Suspended load model
2. Decomposition
3. Estimated effective capture efficiency
Estimate k
Partition k into contributions of settling and capture on collectors
Use kc to estimate effective capture efficiency

## Slide 12: Methods
Flume experiments
  Two experiments: with dowels, without dowels
Model vegetation stems using array of wooden dowels
Sediment added to flume at start of experiment
Instruments:
  Peristaltic pumps
  Acoustic Doppler velocimeter (ADV)
  Sediment traps

## Slide 13: Methods: Flume
Recirculating flume; average flow velocity 5-6 cm/s
5.25 m long x 0.6 m wide channel
0.4 m water depth
False bed converted into “test section” for dowels

## Slide 14: Methods: Dowels
Coat with silicone grease as biofilm analogue
Install in test section in roughly uniform pattern
Approximate dowel density in the test section of 1450 dowels/m2 in dowel treatment

## Slide 15: Methods: Instruments
Peristaltic pumps: sample water at 5-min intervals
ADV: measure flow velocity

## Slide 16: Methods: Instruments
Sediment traps: accumulate settled particles in locations in the test section

## Slide 17: Methods: Sediment
Crushed walnut shell (~silt)
200 g added at start of each experiment

## Slide 18: Methods: Filtering
Samples from peristaltic pump were filtered through glass microfiber filters, dried, and weighed
Sediment mass/sample volume = mass concentration

## Slide 19: Protocol Summary
Install dowels
(if necessary)
2. Fill flume
3. Set up instruments,
sediment traps
4. Input settings,
turn on flume
5. Add sediment
6. Collect data
8. Filter, dry, and weigh
7. Clean flume (sometimes)

## Slide 20: Flume Operation Sample

## Slide 21: Results
Flume sediment transport description (Shields criterion)
Treatment comparison
  Particle capture rates
  Effective capture efficiency
Predictive model comparison

## Slide 22: Results: Sediment transport style