## Slide 1: Observations and implications of artificial vegetation on suspended sediment capture in laboratory flume experiments
Justin Nghiem
2018-19 Undergraduate Honors Thesis
Department of Geography, UC Berkeley
Advisor: Laurel Larsen

## Slide 2: Motivation
Coastal wetlands are facing historically rapid land loss
Mississippi River Delta has lost over 5000 km2 of wetlands since 1930s
Relative sea level rise accelerates loss

## Slide 3: Motivation
Strategy: vegetation enhances retention of transported sediment load
  Based on previous studies [Palmer et al., 2004; Wu et al., 2011; Fauria et al., 2015]
Mathematical models to predict particle capture are valuable tools for wetland management
  Empirical models of Palmer et al. [2004] and Fauria et al. [2015]

## Slide 4: Research Questions
How well do existing models of suspended particle capture by vegetation stems perform?
  Are there important but unaccounted parameters?
For specific conditions, what is the influence of vegetation on suspended particle capture in wetlands?
How do we respond to these questions?

## Slide 5: One method: Flume experiments

## Slide 6: General Terms
Particle capture – general removal of sediment particles from transport in the flow
Collectors – vegetation stems (or stem-like objects) in the flow; their surfaces “collect” particles from the flow
Suspended load – sediment transported in a flow in suspension

## Slide 7: Particle capture mechanisms
Gravitational settling
Direct interception
Diffusional deposition – turbulence, Brownian motion
Inertial impaction – divergence from flowlines

## Slide 8: Effective capture efficiency
Quantifies overall rate of particle capture by collectors

## Slide 9: Suspended load model
In practice, fit an exponential model, a solution of an advection-diffusion equation [Fauria et al., 2015]
where

## Slide 10: Particle capture rate
Particle capture rate k quantifies how fast sediment concentration declines with time
May be decomposed as
Key: separate effects of settling and collectors
where

## Slide 11: Parameter Estimation Summary
1. Suspended load model
2. Decomposition
3. Estimated effective capture efficiency
Estimate k using data
Partition k into contributions of settling and capture on collectors
Estimate effective capture efficiency using kc

## Slide 12: Methods
Flume experiments
  Two experiments: with dowels, without dowels
Model vegetation stems using array of wooden dowels
Sediment added to flume at start of experiment
Instruments:
  Peristaltic pumps
  Acoustic Doppler velocimeter (ADV)
  Sediment traps

## Slide 13: Recirculating Flume
average flow velocity 5-6 cm/s
Transitional flow
5.25 m long x 0.6 m wide channel
0.4 m water depth
False bed converted into “test section” for dowels

## Slide 14: Dowels
Coat with silicone grease as biofilm analogue
Install in test section in roughly uniform pattern
Approximate dowel density in the test section of 1450 dowels/m2 in dowel treatment

## Slide 15: Sediment
Crushed walnut shell (~silt)
200 g added at start of each experiment

## Slide 16: Instruments
Peristaltic pumps: sample water at 5-min intervals
ADV: measure flow velocity during experiments

## Slide 17: Instruments
Sediment traps: accumulate settled particles in locations in the test section

## Slide 18: Filtering Protocol
Samples from peristaltic pump were filtered through glass microfiber filters, dried, and weighed
Sediment mass/sample volume = mass concentration

## Slide 19: Experiment Protocol Summary
Install dowels
(if necessary)
2. Fill flume
3. Set up instruments,
sediment traps
4. Input settings,
turn on flume
5. Add sediment
6. Collect data
8. Filter, dry, and weigh
7. Clean flume (sometimes)

## Slide 20: Flume Operation Sample

## Slide 21: Results
Flume sediment transport description (Shields criterion)
Treatment comparison
  Particle capture rates
  Effective capture efficiency
Predicted vs actual effective capture efficiency

## Slide 22: Sediment transport regime
Shields criterion for initial particle motion
Conclusion: particles travel in suspension, negligible bed load and resuspension
  Supports application of background theory

## Slide 23: Treatment Comparison
For each experiment, model fitted to all peristaltic pump data points
  Insignificant upstream/downstream contrast
Model:

## Slide 24: Treatment Comparison
Treatment | k (x10-4 s-1) | ks (x10-4 s-1) | kc (x10-4 s-1) | (%)
1. No dowels | 1.620 ± 0.0601 | 1.620 ± 0.0601 | NA | NA
2. Dowels | 2.229 ± 0.0924 | 0.4213 ± 0.0092 | 1.808 ± 0.102 | 0.0689 ± 0.0039
Treatment | k (x10-4 s-1) | ks (x10-4 s-1) | kc (x10-4 s-1) | 
1. No dowels | 1.620 ± 0.0601 | 1.620 ± 0.0601 | NA | NA
2. Dowels | 2.229 ± 0.0924 | 0.4213 ± 0.0092 | 1.808 ± 0.102 | 0.0689 ± 0.0039
Compare: particle capture rates due to settling
Compare: particle capture rates due to settling versus capture on collectors
  Order of magnitude differences

## Slide 25: Predicted vs actual η’
Compare predicted effective capture efficiency by two existing power law models to calculated value
where
Palmer et al. [2004]:
Fauria et al. [2015]:

## Slide 26: What do the results imply?
Particle capture mechanisms
  Through comparison of experiments
Predictive models
  Potential for improved accuracy in effective capture efficiency prediction?

## Slide 27: Particle capture mechanisms
Two primary mechanisms:
  Gravitational settling
  Direct interception
Interaction of mechanisms with the presence of dowels due to flow instabilities
Treatment | ks (x10-4 s-1) | kc (x10-4 s-1)
1. No dowels | 1.620 ± 0.0601 | NA
2. Dowels | 0.4213 ± 0.0092 | 1.808 ± 0.102

## Slide 28: Predictive models
Comparable Rec and R for experiments in this study, Palmer et al. [2004], and Fauria et al. [2015]
Different experimental conditions
  Palmer: single cylindrical collector with smooth & rough greased surface
  Fauria: array of emergent collectors with biofilm coating
Model | (%)
Palmer et al. [2004] | 0.142
Fauria et al. [2015] | 0.0261
Dowel treatment | 0.0689
Model | 
Palmer et al. [2004] | 0.142
Fauria et al. [2015] | 0.0261
Dowel treatment | 0.0689

## Slide 29: Predictive models
Alternative model
Add information on vegetation characteristics to kinematic and geometric parameters (Rec & R)
  Interference between many collectors with wake generation
  Particles interact directly with stem surface

## Slide 30: Conclusion
In the two experiments, dowel collectors augment overall particle capture rate
  Interactions of dowels and particle settling
Possible additions to predictive models for effective capture efficiency (stem density and surface)
  Better fit of experiment data to model with similar collector characteristics

## Slide 31: Acknowledgements
Laurel Larsen for her research mentorship
Jordan Wingenroth for his work on the flume and feedback
Yayla Sezginer, Candace Yee, and Dani Satin for assistance in flume experiments
and everyone at the Environmental Systems Dynamics Laboratory for their support

## Slide 32: References
Beckett, Ronald, and Ngoc P. Le. 1990. “The Role or Organic Matter and Ionic Composition in Determining the Surface Charge of Suspended Particles in Natural Waters.” Colloids and Surfaces 44 (January): 35–49. https://doi.org/10.1016/0166-6622(90)80185-7.
Biron, Pascale M., Colleen Robson, Michel F. Lapointe, and Susan J. Gaskin. 2004. “Comparing Different Methods of Bed Shear Stress Estimates in Simple and Complex Flow Fields.” Earth Surface Processes and Landforms 29 (11): 1403–15. https://doi.org/10.1002/esp.1111.
Britsch, Louis D., and Joseph B. Dunbar. 1993. “Land Loss Rates: Louisiana Coastal Plain.” Journal of Coastal Research 9 (2): 324–38.
Brownlie, William R. 1981. “Prediction of Flow Depth and Sediment Discharge in Open Channels.” Report. November 1981. http://resolver.caltech.edu/CaltechKHR:KH-R-43A.
Composition Materials. “200 Mesh Walnut Shell Flour (WF-5).” 2013. Composition Materials Co. July 25, 2013. https://compomat.com/200-mesh-walnut-shell-flour-wf-5.
Discflo. “About Classic – Discflo.” n.d. Accessed April 20, 2019. https://discflo.com/about-classic.
Droppo, I. G., G. G. Leppard, D. T. Flannigan, and S. N. Liss. 1997. “The Freshwater Floc: A Functional Relationship of Water and Organic and Inorganic Floc Constituents Affecting Suspended Sediment Properties.” In The Interactions Between Sediments and Water: Proceedings of the 7th International Symposium, Baveno, Italy 22–25 September 1996, edited by R. Douglas Evans, Joe Wisniewski, and Jan R. Wisniewski, 43–53. Dordrecht: Springer Netherlands. https://doi.org/10.1007/978-94-011-5552-6_5.
Fauria, Kristen E., Rachel E. Kerwin, Daniel Nover, and S. Geoffrey Schladow. 2015. “Suspended Particle Capture by Synthetic Vegetation in a Laboratory Flume.” Water Resources Research 51 (11): 9112–26. https://doi.org/10.1002/2014WR016481.
Fuchs, N. A. 1964. The Mechanics of Aerosols, edited by R. E. Daisley and M. Fuchs. New York: Pergamon.
García, Marcelo H. 2008. “Sediment Transport and Morphodynamics.” In Sedimentation Engineering: Processes, Measurements, Modeling, and Practice - ASCE Manuals and Reports on Engineering Practice (MOP) No. 110, edited by Marcelo H. García, 21-164. Reston: American Society of Civil Engineers. https://doi.org/10.1061/9780784408148.ch02.
Kadlec, Robert H. 1990. “Overland Flow in Wetlands: Vegetation Resistance.” Journal of Hydraulic Engineering 116 (5): 691–706. https://doi.org/10.1061/(ASCE)0733-9429(1990)116:5(691).
Nepf, Heidi M. 1999. “Drag, Turbulence, and Diffusion in Flow through Emergent Vegetation.” Water Resources Research 35 (2): 479–89. https://doi.org/10.1029/1998WR900069.
Nortek. 2019. “Velocimeter for Boundary Velocity Profile Measurements.” Text/html. Nortek. April 26, 2019. https://www.nortekgroup.com/products/vectrino-profiler.
Palmer, Molly R., Nepf Heidi M., Pettersson Thomas J. R., and Ackerman Josef D. 2004. “Observations of Particle Capture on a Cylindrical Collector: Implications for Particle Accumulation and Removal in Aquatic Systems.” Limnology and Oceanography 49 (1): 76–85. https://doi.org/10.4319/lo.2004.49.1.0076.
Purich, Ariaan. 2006. “The Capture of Suspended Particles by Aquatic Vegetation.” PhD diss., School of Environmental Systems Engineering, University of Western Australia. http://www.westerlycentre.uwa.edu.au/__data/assets/pdf_file/0009/1637505/Purich_2007.pdf.
Rubenstein, Daniel I., and M. A. R. Koehl. 1977. “The Mechanisms of Filter Feeding: Some Theoretical Considerations.” The American Naturalist 111 (981): 981–94. https://doi.org/10.1086/283227.
Spielman, Lloyd A. 1977. “Particle Capture from Low-Speed Laminar Flows.” Annual Review of Fluid Mechanics 9 (1): 297–319. https://doi.org/10.1146/annurev.fl.09.010177.001501.
Sutherland, Bruce R., Kai J. Barrett, and Murray K. Gingras. 2015. “Clay Settling in Fresh and Salt Water.” Environmental Fluid Mechanics 15 (1): 147–60. https://doi.org/10.1007/s10652-014-9365-0.
Syvitski, James P. M., Albert J. Kettner, Irina Overeem, Eric W. H. Hutton, Mark T. Hannon, G. Robert Brakenridge, John Day, et al. 2009. “Sinking Deltas Due to Human Activities.” Nature Geoscience 2 (10): 681–86. https://doi.org/10.1038/ngeo629.
Wu, Lei, Bin Gao, and Rafael Muñoz-Carpena. 2011. “Experimental Analysis of Colloid Capture by a Cylindrical Collector in Laminar Overland Flow.” Environmental Science & Technology 45 (18): 7777–84. https://doi.org/10.1021/es201578n.